## Slide 1: Menu Navigation
  Presented by: Tzahi Ezra
  Advisors:
  Moshe Porian
  Netanel Yamin
  One semester project
  Project initiation: NOV 2014
Project’s MID presentation

## Slide 2
Contents
Remainder
Project goal
Conceptual description
Requirements
Top architecture
Background
Micro architecture
Project’s schedule

## Slide 3: Remainder
In the preceding project, the following was implemented:
Generating symbols on display screen using:
  GUI platform - coded with Matlab
  Cyclone II FPGA
  Host communication via UART protocol
  Internal communication via Wishbone protocol
Input - Grayscale symbols 32 x 32 pixels
  saved in external SDRAM
Output - Grayscale image resolution of 800x600 pixels
Main clock freq. 100MHz
VESA (monitor) freq. 40 Hz
Notes: תזכורת:
משתמשים בתשתית של פרויקט קודם.
התקשורת החיצונית בין המערכת למחשב תבוצע באמצעות פרוטוקול UART
התקשורת בין הבלוקים הפנימיים תבוצע בהתאם לפרוטוקול WISHBONE
כל הבלוקים עובדים בתדר של 100 MHz למעט הVesa

## Slide 4: Project’s goal
Navigation in a menu
  Implement blocks in FPGA, coded in Vhdl HDL, for the following functions:
    Displaying the cursor by inverting the pixels of a symbol located in the frame .
    Moving a cursor right, left, up, down the from its current position.
    Navigation in the menu would be performed using HW only, via buttons on the DE2 board.
    In the design, special registers hold the desired cursor position, and synchronization with the GUI is supported, for debug purposes.
    All the blocks would communicate via Wishbone protocol

## Slide 5: Conceptual description
  Symbol insertion/removal & navigation concept
Figure 1.2 – Menu navigation using the buttons on the DE2 board
Figure 1.1 –Symbol insertion/removal using the GUI

## Slide 6: Requirements
Architecture implementation
RTL coding (VHDL)
Simulation (Modelsim)
Synthesis (Quartus)
Place & Route
FPGA implementation

## Slide 7: Top architecture
Navigator
Figure 2 – top architecture
opcode

## Slide 8: Background
Add/Remove a symbol
1 bit
Horizontal Screen Location
(0-19)5 bit
Orthogonal Screen Location
(0-14)4 bit
SDRAM ROW(11), SDRAM BANK(2)
13 bits
6.1 Opcode Structure
Figure 3 – Opcode structure

## Slide 9: 6.2.1 Continuous use:
Notes: 1.המשתמש בוחר את הסימבולים שרוצה להוסיף/להסיר או לבחור בסימבול מסוים ומוסר מידע על מיקומם,
בעזרת פלטפורמת הGUI.
2.המחשב המארח מעביר הודעה שמורכבת מפקטות של מידע על מיקום הסימבול בזיכרון הSDRAM, מיקומו על המסך, והאם הוסף/נגרע/נבחר, אל מסלול הRX. הפקטה לא עוברת בשלמותה אל ה- SG TOP, היא מגיעה ל- RX PATH וזה מקלף לה את header , שומר ערכים כמו length ו- type ברגיסטרים שלו ומעביר את המידע (ה- Payload) לפי ה-type אל עבר היחידה המתאימה.
לאחר מכן המידע עובר אל הRam ומרגע הגעת סיגנל VSYNC (המורה על התחלת הצגת הframe מהפינה השמאלית העליונה), המידע על השינויים מהframe הקודם נשמרים בו. בלוק הManager שבתוך הSG TOP נשלחת בקשת קריאה מהSDRAM, ומשם המידע יועבר אל הVESA Controller Block, בעזרת שימוש בdual clk FIFO, ומשם המידע יעבור אל תצוגת הVGA.
3. סעיף מס' 2 יחזור על עצמו.

## Slide 10: 6.2.2 Continuous use:
INTERCON
Notes: 1.המשתמש לוחץ על אחד הלחצנים שנמצאים בDE2 בורד.
2.ערכי הרגיסטרים של מיקום הסמן מתעדכנים בתגובה ללחיצה.
3. מתוך ערכי הרגיסטרים, נייצר הודעה על מיקום הסמן שתגיע אל מסלול הTX דרך הWISHBONE INTERCONNECT בהתאם לשדה הtype שנגדיר אותו להיות בלוק הTX, וזה יקלף לה את header , ויעביר את המידע (ה- Payload) אל עבר התוכנה.
3. סעיף מס' 2 יחזור על עצמו.

## Slide 11
  Display controller top diagram:
6.3 Display Controller
Figure 6 – display controller inner implementation
SG

## Slide 12
6.4 Symbol generator top
Figure 7 – symbol generator inner implementation
Navigator
inversion

## Slide 13: Micro architecture
  The following diagram shows a general scheme of the navigator block and its interconnection to DE2
  buttons
DE2
7.1 Navigator block
Figure 8 – project’s main scheme

## Slide 14
7.2 x_y_location states table
down |  | up |  | left |  | right |  |  | 
Next state |  |  |  |  |  |  |  | Curr. state | 
Y | X | Y | X | Y | X | Y | X | Y | X
1 | 0 | 14 | 1 | 14 | 19 | 0 | 1 | 0 | 0
1 | 19 | 14 | 19 | 0 | 18 | 1 | 0 | 0 | 19
0 | 18 | 13 | 19 | 14 | 18 | 0 | 0 | 14 | 19
0 | 0 | 13 | 0 | 13 | 19 | 14 | 1 | 14 | 0
1 | X | 14 | X+1 | 0 | X-1 | 0 | X+1 | 0 | 1..18
19 | Y+1 | 19 | Y-1 | Y-1 | 18 | Y+1 | 0 | 1..13 | 19
0 | X-1 | 13 | X | 14 | X-1 | 14 | X+1 | 14 | 1..18
Y+1 | 0 | Y-1 | 0 | Y-1 | 19 | Y | 1 | 1..13 | 0
Y+1 | X | Y-1 | X | Y | X-1 | Y | X+1 | 1..13 | 1..18
Table 1– x_y_location states

## Slide 15
DE2
0.1
0.2
0.3
0.4
debouncer
debouncer
debouncer
debouncer
  The following animation shows the process where only when the user presses a button for at least 0.5 sec (changeable), then the debouncer outputs a pulse that updates the X,Y values according to the button pressed
  ( , ).
Figure 5 – buttons pressing concept
7.2 DE2 buttons pressing concept
0.5

## Slide 16
7.5 Debouncer block
Figure 11 – debouncer top block
The debouncer top block diagram:

## Slide 17
The debouncer is a counter which counts how long its input is '1', and triggers when it reaches a defined value (in our case, 0.5 sec is used). It works with the system frequency (100 MHz) such that when it reaches the defined value, its output turns from '0' to '1' for 1 period, than return to '0'.
7.5.1 Debouncer block operation

## Slide 18
7.1.1 Manager block
Figure 8.1 – new manager block with Symbol inversion and cond blocks
The Symbol inversion unit, and Cond unit, were added to the Manager block, to enable the symbol selection by
inverting its pixels, when the internal count of sym_row (symbol row) and sym_col (symbol column), equals to
the value of Hor_out, Ver_out (horizontal and vertical symbol’s location or X,Y registers value) from the
Managing Marker block.
Symbol inversion
Cond

## Slide 19
Symbol inversion
Figure 10– debouncer top block
7.4 Symbol inversion block
The Symbol inversion top block diagram:
pixel(7:0)
data_out(7:0)
Cond

## Slide 20
Marking of a symbol would be responded by inverting the symbol pixels (32*32).
In the manager block, the information of each pixel of the chosen symbol, being read from the SDRAM is inverted before being written to the fifos and passed to the VESA display. Using a mux as shown in the figure below, the pixel itself or its inverted version are chosen to be the data_out. The Cond would be ‘1’ if the internal row and column that are being calculated (represent the current displayed symbol) matches the desired marker symbol’s location.
7.4.1 Symbol inversion block inner implementation
Figure 10.1 – symbol inversion block inner implementation
data_out(7:0)

## Slide 21
7.6 x_y_location_top block
Figure 12 –x_y_location_top block

## Slide 22
7.6.1 x_y_location_top block inner implementation
Figure 12.1 – x_y_location_top inner implementation
The following diagram represent the block's inner implementation.
This block consists of 2 building blocks: x_y_location block and update upon vsync block. The first is used to determine and hold the cursor location due to buttons presses, and the second is used to update the location, only upon vsync signal arrival.

## Slide 23
7.6 x_y_location block
Figure 12 –x_y_location block
The x_y_location block diagram:

## Slide 24
The following diagram represent the block's inner implementation.
This block uses an FSM to manage its operation.
7.6.1 x_y_location block inner implementation
Figure 12.1 – x_y_location inner implementation

## Slide 25
7.7 update_upon_vsync block
Figure 13 –update_upon_vsync top block

## Slide 26
7.7.1 update_upon_vsync block operation
This block responsible for outputting an updated X, Y values for cursor location, only upon vsync signal arrival.
When vsync signal is triggered high, the horizontal and vertical location output would take x, y
values accordingly, when reset is triggered high x, y would be all zeros, and else the outputs
keep their previous values.

## Slide 27: Project’s schedule
Date | Goals
13/11/2014 – 31/21/2014 | Project Characterization& Prior Study Conduction
31/12/2014 | Characterization Presentation
31/12/2014 – 26/1/2015 | Full Characterization of all blocks
26/1/2015 – 31/3/2015 | Exam period
31/3/2015 – 07/5/2015 | Characterization & RTL Coding (VHDL)
07/5/2015 | Mid presentation
07/5/2015 – 21/7/2015 | RTL Coding (VHDL) and simulation
21/7/2014 –21/8/2015 | Synthesis, FPGA implementation & HW debug
21/8/2015 | Final presentation